## Slide 1
The COAWST Toolbox
COAWST Workshop 2019
NCSU
Notes: ONR

## Slide 2
The COAWST Toolbox: What are the components needed for an arbitrary model setup?
Notes: ONR

## Slide 3
1) grid
Notes: ONR

## Slide 4
2) initial condition: T, S, η, u, v, sediment, vegetation, waves
Notes: ONR

## Slide 5
3) atmospheric forcing
LW, SW
radiation
winds
precipitation
air temperature
humidity
stresses
Notes: ONR

## Slide 6
4) boundary forcing
LW, SW
radiation
winds
tides
incoming or
outgoing
currents, T,
S, sediment
waves
precipitation
air temperature
humidity
stresses
Notes: ONR

## Slide 7
5) climatology
LW, SW
radiation
winds
precipitation
air temperature
humidity
tides
incoming or
outgoing
currents, T,
S, sediment
waves
Notes: ONR

## Slide 8
The COAWST Toolbox: What is it?
suite of MATLAB tools, scripts, and functions distributed with COAWST via svn
provides standard functionality to create grids, initial condition, boundary, and climatology files, atmospheric forcing files, tidal forcing files
ROMS expects specific variable names, dimensions, units, netcdf conventions
  check varinfo.dat
SWAN expects specific file formats
  check SWAN User Manual
Notes: ONR

## Slide 9
The COAWST Toolbox: What is it?
other very useful toolboxes are also distributed within
utility, analysis, plotting routines
  tidal analysis
  map generation
Notes: ONR

## Slide 10
The COAWST Toolbox: What is it?
recommended approach:
add the toolbox to your MATLAB path
copy overarching (master) functions to your own folder for editing for your application
Notes: ONR

## Slide 11
The COAWST Toolbox: Where is it?
[~/COAWST]$ ls
coawst.bash Lib run_coawst WRF
COAWST_User_Manual.doc makefile SOILPARM.TBL WW3
Compilers Master SWAN
Data Projects Tools
ESM REFDIF URBPARM.TBL
GENPARM.TBL ROMS User
InWave RRTM_DATA VEGPARM.TBL
LANDUSE.TBL RRTM_DATA_DBL WPS
Notes: ONR

## Slide 12
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 13
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 14
The COAWST Toolbox: inwave_tools
[~/COAWST/Tools/mfiles/inwave_tools/]$ ls
Bound_wave.m InWave_inlet_test_param.m plot_bound_wave.m
create_InWave_bry.m InWave_lip_param.m read_swan_spc.m
create_InWave_grd.m InWave_shoreface_param.m specchar.m
create_InWave_ini.m jonswap_lip.m waven.m
freq_test.m master_InWave_create_files.m
groupchar.m offbreach_2012103100.spc2d
InWave is an infragravity wave model that uses SWAN S(ƒ,θ) to generate and propagate infragravity wave energy
scripts to build test cases (master_*.m, InWave_*_param.m, create_InWave_*.m)
scripts to calculate wave characteristics (waven.m, specchar.m, freq_test.m, …)
Notes: ONR

## Slide 15
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 16
The COAWST Toolbox: m_map
[~/COAWST/Tools/mfiles/m_map/]$ ls
Contents.m m_etopo2.m m_idist.m m_range_ring.m m_usercoast.m
m_annotation.m m_etopo2.m.OLD m_jet.m m_rectangle.m m_utmgrid.m
map.html m_fdist.m m_legend.m m_ruler.m m_vec.m
mapug.html m_geo2mag.m m_line.m m_scale.m m_windbarb.m
m_coast.m m_geodesic.m m_ll2xy.m m_scatter.m m_xy2ll.m
m_colmap.m m_grid.m m_lldist.m m_shadedrelief.m m_xydist.m
m_contfbar.m m_gshhs_c.m m_mag2geo.m m_shaperead.m mygrid_sand2.m
m_contourf.m m_gshhs_f.m m_patch.m m_streamline.m private
m_contour.m m_gshhs_h.m m_pcolor.m m_tba2b.m wysiwyg.m
m_coord.m m_gshhs_i.m m_plotbndry.m m_tbase.m
m_demo.m m_gshhs_l.m m_plot.m m_text.m
m_elev.m m_gshhs.m m_proj.m m_track.m
m_ellipse.m m_hatch.m m_quiver.m m_ungrid.m
https://www.eoas.ubc.ca/~rich/map.html
mapping functionality for MATLAB
Notes: ONR

## Slide 17
The COAWST Toolbox: m_map
Notes: ONR

## Slide 18
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 19
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
Notes: ONR

## Slide 20
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
Notes: ONR

## Slide 21
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
calculates the distance in m between two lat/lon points
Notes: ONR

## Slide 22
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
time functionality
Notes: ONR

## Slide 23
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
vertical coordinates
functionality
Notes: ONR

## Slide 24
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
loads an entire netcdf file
Notes: ONR

## Slide 25
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
pcolor that doesn’t clip data in interpolation
Notes: ONR

## Slide 26
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
fills missing data via a filter
Notes: ONR

## Slide 27
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
Notes: ONR

## Slide 28
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
creates SWAN .bot and .grd from roms grid
Notes: ONR

## Slide 29
The COAWST Toolbox: mtools
[~/COAWST/Tools/mfiles/mtools/]$ ls
create_extra_rho_grid.m ncei_2roms.m
create_roms_child_clm.m ncei_2swan.m
create_roms_child_init.m netcdf_load.m
create_roms_forcings.m parentchild_bathy.m
create_roms_init.m parentchild_mask.m
create_roms_netcdf_grid_file.m pcolorjw.m
create_roms_rivers.m plot_scrip_weights.m
create_roms_xygrid.m roms2swan.m
create_ww3_grid_files.m roms_getnplot_grid_rutgers.m
create_ww3_wind_forcing.m s2hms.m
earthdist.m set_depth.m
gregorian.m stretching.m
ij2ind.m swanmat2roms.m
ind2ij.m sw_dist.m
julian.m sw_f.m
maplev.m wrf2roms_mw.m
mat2roms_mw.m wrf_rename.plx
narrnc2roms.m
Notes: ONR

## Slide 30
The COAWST Toolbox: mtools
https://www.ncdc.noaa.gov/data-access/model-data/model-datasets
extracts atmospheric variables from the chosen product
GFS
  Global
  analysis and forecast
  products
  2007-present
NARR
  North American
  reanalysis product
  1979-2014
NAM
  North American
  analysis and forecast
  products
  2004-present
Notes: ONR

## Slide 31
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 32
The COAWST Toolbox: roms_clm
[~/COAWST/Tools/mfiles/mtools/roms_clm/]$ ls
create_roms_netcdf_bndry_mwUL.m roms_from_stdlev_mw.m
create_roms_netcdf_clm_mwUL.m roms_master_climatology_coawst_mw.m
create_roms_netcdf_init_mw.m roms_zint_mw.m
dirsort.m u2rho_2d_mw.m
get_ijrg.m u2rho_3d_mw.m
rho2u_2d_mw.m updatbdry_coawst_mw.m
rho2u_3d_mw.m updatclim_coawst_mw.m
rho2v_2d_mw.m updatinit_coawst_mw.m
rho2v_3d_mw.m v2rho_2d_mw.m
roms_cgridpos.m v2rho_3d_mw.m
roms_combine_clm_bdy.m
Notes: ONR

## Slide 33
The COAWST Toolbox: roms_clm
HYCOM (Hybrid Coordinate Ocean Model)
  data assimilative
  1/12° resolution
  hybrid vertical coordinates
  excellent source for initial, boundary, and climatology conditions
Notes: ONR

## Slide 34
The COAWST Toolbox: roms_clm
HYCOM (Hybrid Coordinate Ocean Model)
  data assimilative
  1/12° resolution
  hybrid vertical coordinates
  excellent source for initial, boundary, and climatology conditions
Notes: ONR

## Slide 35
The COAWST Toolbox: roms_clm
find the lat/lon range of your grid within the HYCOM domain
initialize the climatology, boundary, and initial conditions netcdf files
extract HYCOM u, v, η, T, S within the lat/lon range found
  transform vertical coordinates
  calculate ubar, vbar
  rotate to your ROMS grid
write out initial fields
append climatology fields for time period and frequency requested
write boundary fields
Notes: ONR

## Slide 36
The COAWST Toolbox: roms_clm
[~/COAWST/Tools/mfiles/mtools/roms_clm/]$ ls
create_roms_netcdf_bndry_mwUL.m roms_from_stdlev_mw.m
create_roms_netcdf_clm_mwUL.m roms_master_climatology_coawst_mw.m
create_roms_netcdf_init_mw.m roms_zint_mw.m
dirsort.m u2rho_2d_mw.m
get_ijrg.m u2rho_3d_mw.m
rho2u_2d_mw.m updatbdry_coawst_mw.m
rho2u_3d_mw.m updatclim_coawst_mw.m
rho2v_2d_mw.m updatinit_coawst_mw.m
rho2v_3d_mw.m v2rho_2d_mw.m
roms_cgridpos.m v2rho_3d_mw.m
roms_combine_clm_bdy.m
Notes: ONR

## Slide 37
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 38
The COAWST Toolbox: rutgers
[~/COAWST/Tools/mfiles/rutgers/]$ ls
4dvar bin coastlines forcing initial netcdf
bathymetry boundary colormaps grid landmask seawater
utility
ROMS-distributed toolbox
Notes: ONR

## Slide 39
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 40
The COAWST Toolbox: swan_forc
[~/COAWST/Tools/mfiles/swan_forc/]$ ls
bdry_com.m ww3gb_2TPAR.m
createswan2Dspec.m ww3partition_2TPAR.m
extract_and_save_WW3_partitioned_data.m ww3_specpoints.m
extract_partition_data_awk_westcoast.sh ww3_swan_input.m
Read_SWAN_Dspec.m WWIIIpartitioned2full2D.m
Notes: ONR

## Slide 41
The COAWST Toolbox: swan_forc
NCEP WaveWatch3
Identify points along the boundary where bulk wave parameters or 2D spectra will be defined
Extract either bulk wave parameters or partitioned data which will be reconstructed into spectra
Write to appropriate file format for SWAN to read
Provide user commands for swan.in file
Notes: ONR

## Slide 42
The COAWST Toolbox: swan_forc
[~/COAWST/Tools/mfiles/swan_forc/]$ ls
bdry_com.m ww3gb_2TPAR.m
createswan2Dspec.m ww3partition_2TPAR.m
extract_and_save_WW3_partitioned_data.m ww3_specpoints.m
extract_partition_data_awk_westcoast.sh ww3_swan_input.m
Read_SWAN_Dspec.m WWIIIpartitioned2full2D.m
Notes: ONR

## Slide 43
The COAWST Toolbox: What is in it?
[~/COAWST/Tools/mfiles/]$ ls
inwave_tools
m_map
mtools
roms_clm
rutgers
swan_forc
tides
Notes: ONR

## Slide 44
The COAWST Toolbox: tides
[~/COAWST/Tools/mfiles/tides/]$ ls
create_roms_tides.m roms_tide_forc_file.m tidal_ellipse t_tide
Notes: ONR

## Slide 45
The COAWST Toolbox: tides
[~/COAWST/Tools/mfiles/tides/]$ ls
create_roms_tides.m roms_tide_forc_file.m tidal_ellipse t_tide
generate ADCIRC or TPXO tidal forcing
Notes: ONR

## Slide 46
The COAWST Toolbox: tides
[~/COAWST/Tools/mfiles/tides/]$ ls
create_roms_tides.m roms_tide_forc_file.m tidal_ellipse t_tide
Notes: ONR

## Slide 47
The COAWST Toolbox: general format for master scripts
% script ww3_swan_input.m
%
% This script is the main driver to
% download, convert and interpolate WW3 data to TPAR input for SWAN.
%
% Written 4/23/09 by Brandy Armstrong
% some mods, jcwarner Arpil 27, 2009
% added partition file call, jcw, 04Feb2019
%
% First, acquire the necessary grib, ascii (gz), or nc files from
% ftp://polar.ncep.noaa.gov/pub/history/waves/

## Slide 48
The COAWST Toolbox: general format for master scripts
% ************* BEGIN USER INPUT ****************************
% 1) Enter WORKING DIRECTORY.
% This is the location of ww3 files downloaded and the
% location of output for the forcing files to be created.
%
working_dir='F:\data\models\COAWST_tests\coawstv3.4_update\coawst_v3.4_tests\sandy\Projects\Sandy\ww3'
% 2) Enter start dates of data requested.
yearww3='2012'; %input year of data yyyy
mmww3='10'; %input month of data mm
ddww3='00'; %keep this as '00’

## Slide 49
The COAWST Toolbox: general format for master scripts
% flag for simulations that span several months.
% 0 = one month, 1 = more than one month
% This long run flag is only coded for TPAR files for now.
long_run=0;
if long_run
total_number_months=2; % total number of months
% (not the length of the run, but rather the number
% of ww3 files)
end
% 3) Enter path\name of SWAN grid. This is set up to use the roms grid as the same for swan.
modelgrid='F:\data\models\COAWST_tests\coawstv3.4_update\coawst_v3.4_tests\sandy\Projects\Sandy\Sandy_roms_grid.nc';

## Slide 50
The COAWST Toolbox: general format for master scripts
% 5)
% Here you decide to use gridded field output (to make TPAR) or spectral partition data (to make 2Dspec). Read this:
% ftp://polar.ncep.noaa.gov/pub/history/waves/multi_1/00README
% Pick one of these:
use_field_output=0; % will create TPAR files.
use_partition_data=1; % will create 2D spec files.
if (use_field_output)
% Enter the ww3 grid area
ww3_area='multi_1.at_10m'; %western north atlantic
end
if (use_partition_data)
% Enter name of wave watch 3 partition file
partfile='multi_1.partition.glo_30m.201210';
end
% *************END OF USER INPUT****************************

## Slide 51
The COAWST Toolbox
Common issues:
  atmospheric forcing, climatology, boundary, initial condition files
  file formats, variable names, etc. change over the years
  check THREDDS catalogs
For help:
  ROMS forum
  COAWST forum
  email
Future developments:
  github version control and community contribution
Notes: ONR