## Slide 1: INWAVE: THE INFRAGRAVITY WAVE DRIVER OF COAWST
COAWST WORKSHOP
Raleigh, 25th -28th February, 2019
Maitane Olabarrieta
John C. Warner
Christie Hegermiller

## Slide 2
OUTLINE
  INTRODUCTION AND MOTIVATION
  IG WAVE GENERATION AND DISSIPATION MECHANISMS
  IG WAVE MODELING TECHNIQUES
  INWAVE
    a. EQUATIONS AND NUMERICAL SCHEME
    b. HOW IS IT LINKED TO THE VORTEX FORCE?
    c. APPLICATIONS
    d. FUTURE PLANS

## Slide 3
Storms, tsunamis
Wind
Sun, Moon
Frequency (Cycles per second)
24 h
12 h
5 min
30 s
1 s
0.1 s
Shallow water waves
Intermediate and deep water waves
Coriolis
Gravity
Surface Tension
Restoring Force
Forcing
Tides
Long Waves
Kind of Wave
Infra-gravity Waves
Gravity Waves
Ultra-gravity Waves
Capillarity Waves
Period
Energy
OCEAN
ROMS SST
INTRODUCTION AND MOTIVATION
Gravity Waves
SWAN Hsig

## Slide 4
InfraGravity (IG) waves are defined as waves with periods between 30 and 300 seconds generated by the non-linear interactions of gravity waves.
In deep water the energy transfer to IG waves is non-resonant and the height of the IG waves is few millimeters. In shallow water the energy transfer becomes near-resonant and IG wave height can increase to over 1 m.
IG waves are highly correlated with the modulation of wind or swell waves.
INTRODUCTION AND MOTIVATION

## Slide 5
RUNUP AND BEACH-DUNE EROSION
HARBOR RESONANCE
INTRODUCTION AND MOTIVATION
HYDRODYNAMICS IN CORAL REEFS

## Slide 6
INTRODUCTION AND MOTIVATION
sea-swell
infragravity
≈ 15%
offshore
surfzone
tides
Ruessink, B.G. (2010). Observations of turbulence within a natural surf zone. Journal of physical oceanography, 40 (12).

## Slide 7
TOTAL WATER LEVEL=
ASTRONOMIC TIDE (AT) + STORM SURGE (SS) + WAVE RUNUP
atmospheric pressure +
wind stress +
shelf oscillations or seiche
wave setup +
incident wave runup +
IG wave runup
INTRODUCTION AND MOTIVATION

## Slide 8
IG WAVE GENERATION AND DISSIPATION MECHANISMS
GENERATION MECHANISMS
GROUP-BOUND WAVE GENERATION AND SHOALING: Quadratic difference interaction among pairs of primary waves, resulting in group-bound second-order waves (Biesel, 1952; Longuet-Higgins and Stewart, 1962).
Figure taken from Bertin et al. (2018) Infragravity waves: from driving mechanisms to
Impacts. Earth science reviews.

## Slide 9
IG WAVE GENERATION AND DISSIPATION MECHANISMS
Incident wave group
Incoming and outgoing free long wave
Incident wave groups
Breaking point
Reflection
Incoming bound long wave
Outgoing free long wave
Dominant over mild slopes
z
x (cross-shore direction)

## Slide 10
IG WAVE GENERATION AND DISSIPATION MECHANISMS
BREAK-POINT MOVEMENT: Symonds et al., 1982; Symonds and Bowen, 1984, Schaffer and Jonsson, 1990 and Schaffer, 1990.
Dominant over steep slopes
Incident wave groups
Breaking point variation
Breakpoint
Setup
Wave height
z
x (cross-shore direction)
Outgoing breakpoint forced long wave
Shoreward breakpoint forced long wave

## Slide 11
IG WAVE GENERATION AND DISSIPATION MECHANISMS
Breaking point variation
Breakpoint
Setup
Wave height
The highest waves in the wave group produce a higher
setup than the smallest waves: wave group modulation
of the wave setup
z
x (cross-shore direction)
Incident wave groups

## Slide 12
IG WAVE GENERATION AND DISSIPATION MECHANISMS
3. BORE MERGING or BORE-BORE CAPTURE (BBC) MECHANISM: Huntley and Bowen, 1975; Huntley and Bowen, 1974; Bradshaw, 1980; Mase, 1989; Sénéchal et al. 2001; Marche et al., 2007; Tissier et al. 2017 ….
for the bichromatic wave case A-1 from van Noorloos (2003) lab experiment
Tissier et al. 2017

## Slide 13
IG WAVE GENERATION AND DISSIPATION MECHANISMS
GENERATION MECHANISMS
Battjes, J. A., H. J. Bakkenes, T. T. Janssen, and A. R. van Dongeren (2004),
Shoaling of subharmonic gravity waves, J. Geophys. Res., 109, C02009.
Breakpoint mechanism is dominant over steep slopes
Bound-wave shoaling is dominant over mild-slopes
BBC or Bore merging seems to be a less dominant mechanism for IG wave generation (according to the results of Tissier et al., 2017)

## Slide 14
IG WAVE GENERATION AND DISSIPATION MECHANISMS
DISSIPATION MECHANISMS
Bottom friction (Henderson and Bowen, 2002; de Bakker et al., 2014).
Non-linear energy transfer back to sea-swell frequencies through triad interaction (Henderson et al., 2006; Thomson et al., 2006; Guedes et al., 2013).
IG wave breaking (Battjes et al., 2004; Van Dongeren et al., 2007; Lin and Hwung, 2012; Nazaka and Hino, 1991).
Energy transfer thru non-linear interactions to lower periods.
It is not clear which is the main dissipation mechanism and it might depend on the beach slope and on the frequency of the IG components.

## Slide 15
IG WAVE MODELLING TECHNIQUES
MODELLING APPROACHES OR TECHNIQUES
WAVE RESOLVING TECHNIQUES:
BOUSSINESQ , PARTICLE METHODS, NON-HYDROSTATIC MODELS OR RANS MODELS
WAVE AVERAGED OR PHASE AVERAGED TECHNIQUES:
WAVE ACTION BALANCE EQUATION + NLSW

## Slide 16
IG WAVE GENERATION AND DISSIPATION MECHANISMS

## Slide 17
Dimension | Short wave resolving | Short wave averaged | LSWE | NSWE | RANS | NH | BSNQ | WKB
1D | 2,7,8 | 1,30,3,5,9 | 1,5,9 | 2,30,3 |  |  | 7,8 | 
1D+ |  | 10,11,25,26 | 10,11,26 |  |  |  |  | 25
2DH | 18,17, 32 | 15,14,23 |  | 15,14,23 |  |  | 18,17,32 | 
2DV | 33 |  |  |  | 33 |  |  | 
Q3D |  | 30 |  | 30 |  |  |  | 
3D | 22 | 19 |  | 19 |  | 22 |  | 
IG WAVE MODELLING TECHNIQUES
Modeling approaches:
from Reniers, 2012 (Long Wave and Runup Workshop)

## Slide 18
SWAN or WW III
DOMAIN
INWAVE
INWAVE IS BASED ON THE WAVE-AVERAGED OR PHASE-AVERAGED TECHNIQUE
INWAVE IS SIMILAR TO XBEACH MODEL (Roelvink et al., 2009) BUT WITH THE DIFFERENCE
THAT INWAVE+ROMS IS ABLE TO SIMULATE 3D CIRCULATION
DIRECTIONAL WAVE SPECTRUM
Wave group time scale
Boundary region
SWAN/WWIII domain: Wave spectral time scale
INWAVE DOMAIN

## Slide 19
FREE SURFACE ELEVATION AND WAVE ENERGY ENVELOPE TIME VARIATION
Wave group scale varying
Wave forcing
Infragravity wave generation +
3D hydrodynamics
Boundary condition for the wave action conservation equation
Vortex Force terms varying in wave group scale
INWAVE

## Slide 20
USE THE GROUP VARYING WAVE ENERGY FORCING AS INPUTS
FOR THE VORTEX-FORCE (VF) IN ROMS
Infragravity wave generation thru VF and propagation of the bound IG wave
Leaky, bound and trapped infragravity waves
ROMS
INWAVE
MAIN MODULES OF INWAVE
READ SWAN DIRECTIONAL
SPECTRAL OUTPUTS AT
THE CHILD GRID BOUNDARIES
RECONSTRUCT THE GROUP SCALE
VARYING WAVE ACTION TIME SERIES
AT THE CHILD GRID BOUNDARY
PROPAGATE IN TIME AND SPACE
THE GROUP VARYING WAVE
ENERGY AT THE CHILD GRID
RECONSTRUCT THE INCOMING
BOUND INFRAGRAVITY WAVES
(e.g. Herbers et al. 1994)

## Slide 21
RANDOM PHASES +
INVERSE FFT
HILBERT TRANSFORM +
LOW-PASS FILTER
INWAVE
For each realization A(x,y,θ,t) is going to be different
Notes: x = hilbert(xr) returns a complex helical sequence, sometimes called the analytic signal, from a real data sequence. The analytic signal x = xr + i*xi has a real part, xr, which is the original data, and an imaginary part, xi, which contains the Hilbert transform. The imaginary part is a version of the original real sequence with a 90° phase shift. Sines are therefore transformed to cosines and vice versa. The Hilbert transformed series has the same amplitude and frequency content as the original real data and includes phase information that depends on the phase of the original data.

## Slide 22
Van Dongeren et al. (2003) -> Hasselman (1963) & Herbers et al. (1994)
1. The energy of the secondary forced elevation E3 (Df) for one particular pair of interacting primary waves can be computed following Herbers et al. (1994)
Amplitude of the bound wave for each interacting pair
2. Bound wave out of phase with the envelope formed by each interacting pair
4. The time series of the surface elevation of the bound wave is
3. The direction of the bound wave is give by
5. This process is repeated for every pair of short-wave components. The summation of all components gives the total bound wave.
INWAVE
RECONSTRUCT THE INCOMING BOUND INFRAGRAVITY WAVES

## Slide 23
Wave action balance equation in Cartesian coordinate system
Wave dispersion relation + Doppler relation
Eikonal equation
INWAVE

## Slide 24
Roelvink (1993)
H= γh
Wave breaking
INWAVE
]
]
Roelvink, J.A., 1993. Dissipation in random wave groups incident on a beach. Coastal Eng., 19:127- 150.

## Slide 25
Horizontal space
INWAVE

## Slide 26
Directional space
1
2
3
4
5
6
ND
1
2
3
ND
ND-1
INWAVE

## Slide 27
Driver_inwave.F
mod_inwave_bound.F
mod_inwave_params.F
mod_inwave_swan.F
mod_inwave_vars.F
get_inwave_bnd_grid.F
get_inwave_data.F
get_inwave_grid.F
get_inwave_ini.F
interp2d.F
math_tools.F
set_inwave_data.F
set_inwave_swan_data.F
swan_reader.F
inwave_globaldefs.h
celer_inw.F
corstep_inw.F
curr_inw.F
dispersion_inw.F
dissip_inw.F
frc_inw.F
prestep_inw.F
Matlab files for test cases inputs
AC3dbc_im.F
ct3dbc_dir_im.F
ct3dbc_im.F
cx3dbc_im.F
cy3dbc_im.F
Tr3dbc_im.F
INWAVE
COAWST
TOOLS
mfiles
Inwave_tools

## Slide 28
/* Master list of all InWave cpp options
*# define INWAVE_MODEL turn ON or OFF InWave model
*# define INWAVE_SWAN_COUPLING turn ON or OFF InWave SWAN coupling
*# define DOPPLER turn ON or OFF the effect of currents on the dispersion relation
*# define ACX_ADVECTION turn ON or OFF advection of Ac in the xi direction
*# define ACY_ADVECTION turn ON or OFF advection of Ac in the etai direction
*# define ACT_ADVECTION turn ON or OFF advection of Ac in the directional direction
*# define WDISS_GAMMA turn ON or OFF energy dissipation
*# define WDISS_ROELVINK turn ON or OFF Roelvink energy dissipation
INWAVE
H= γh
WDISS_GAMMA
WDISS_ROELVINK

## Slide 29
INWAVE_SHOREFACE TEST CASE
INWAVE
Matlab files for test cases inputs: master_Inwave_create_files.m
Inwave_tools
STEP 1
STEP 2
make_Inwave_grd=1;
make_Inwave_ini=1;
make_Inwave_bry=1;
Edit and run InWave_shoreface_param.m

## Slide 30
INWAVE_SHOREFACE TEST CASE
INWAVE
(m)
create_Inwave_grd.m
dx, dy, x, y, depth, angle,
Masking, f, spherical
create_Inwave_ini.m
Nbinds
Ta
Ac_ini
C_ini
create_Inwave_bnd.m
Ta1=10 s, a1= 1 m
Ta2= 8.3 s, a2=0.5 m
Θ= 261 degrees
Hrms_max= 3 m

## Slide 31
INWAVE_SHOREFACE TEST CASE
INWAVE
STEP 3
STEP 4
Edit the file Projects/inwave_shoreface.h and compile COAWST
Edit the file Projects/InWave_shoreface/ocean_inwave_shoreface.in
CCP OPTIONS

## Slide 32
INWAVE
ocean_inwave_shoreface.in

## Slide 33
INWAVE
GRDNAME
IWININAME
BRYNAME
STEP 5
RUN!

## Slide 34
INWAVE
β=1.18
Steep-slope regime: breakpoint generation dominance

## Slide 35
INWAVE
What do we get for the equivalent wave field but without wave-groups?

## Slide 36
INWAVE
With wave-groups

## Slide 37
2DV CASE: DELTA FLUME EXPERIMENT T04 FROM DELTARES
INWAVE
Figures from Van Gent el at., 2008
Pierson-Moskowitz
Hm0=1.5 m
Tp= 7.35 s
Tm= 6.68 s

## Slide 38
COAWST- MEASUREMENTS COMPARISON
RMSE=0.15 m
RMSE=0.07 m/s
RMSE=0.02 m
RMSE=0.1 m
INWAVE

## Slide 39
Time at 0.1, 0.3, 1, 2, and 6 hours
INWAVE
MORPHODYNAMIC EVOLUTION

## Slide 40
INWAVE
MEAN WAVE-AVERAGED CURRENTS
m/s

## Slide 41
3D CASE REAL APPLICATION: HURRICANE SANDY (2012)
INWAVE
http://storms.ngs.noaa.gov/storms/sandy/

## Slide 42
Breach occurred at
"Old Inlet"
Was open between 1763 and 1827.
Re-opened during H Sandy.
Still open today.
http://coastal.er.usgs.gov/hurricanes/sandy/photo-comparisons/
INWAVE
Breach occurred at "Old Inlet“ Was open between 1763 and 1827.
Re-opened during H Sandy. Still open today.

## Slide 43
Modeling system grids used for coupled concurrent numerical simulations of oceanographic, wave, and sediment transport processes. The grids have regions of increased refinement to allow greater resolution in selected locations.
COAWST model application
USEast grid
(5-km res.)
New York Bight
grid (700-m res.)
Shelf grid
(100-m res.)
Breach grid
(5-10 m res.)
INWAVE
Notes: A) 5 km resolution USEast grid: Dashed magenta lines indicate where we set the wave boundary conditions based on the global wave model WaveWatchIII. Black rectangle shows the extent of the 700 m resolution New York Bight grid.
B) 700 m resolution New York Bight grid: Black rectangle shows the extent of the 100 m resolution Fire Island Shelf grid.
C) 100 m resolution Fire Island Shelf grid: Black lines show the extent of the 5-40 m resolution Fire Island Strip grid.
D) 5-40 m resolution Fire Island Strip grid: Only a 15-km (alongshore) section near the 2014 Experiment platforms are shown.
'x' in A&B indicates the location of the NDBC Buoy#44066
'square' in B indicates the location of the NDBC Buoy#44065
'circle' in B indicates the location of the NDBC Buoy#44025
'triangle' in B indicates the location of the NDBC Buoy#44017
'dots' in B&C&D indicate the locations of the platforms in the 2014 Experiment.

## Slide 44
INWAVE

## Slide 45
Back bay
Offshore
simulate peak storm intensity
Infragravity wave (0.8m)
Surge (1.5m)
Tide (1.0m)
MSL (0.0m)
Elevation (m)
Cross Shore distance (m)
Use 2D spectra from Offshore point to drive InWave
INWAVE
Notes: RM lower right ?

## Slide 46: InWave Fire Island breach simulations
Grid Setup
480 cells x-dir
439 cells y-dir
dx ~ 5m
dy ~ 20m offshore to 3m dunes
Use 25 directional bins, 10 deg ea., 50:290
Physics:
Roller model (Reniers et al., 2004)
Dissipation (Roelvink et al., 1993)
Vortex Force
UV_KIRBY
SSW BBL (wave enhanced)
Suspended load
Bedload van Der A
Sed Avalanching
Boundary Conditions:
West/East: Water level
North: Water level
South: Water level, BoundWave, AC
Ocean
Land
Depth (m)
INWAVE

## Slide 47
(Hs=7.8m)
Start with a 2D spectra
distribute the time series weighted back into directional bins
- integrate over directions
- compute amplitude of each frequency.
- phase is 2*pi*f + random component.
- add up all freq and compute a water level time series.
impose wave action density
(wave group envelope)
Energy (E) = 1/8 r g (2h)2;
WaveAction (A) = E/(2p/T);
INWAVE

## Slide 48: Wave heights and water levels
~ 1 km
Waves are long crested – need to phase along open boundary.
Offshore currents driven westward from winds
Nearshore currents driven eastward from breaking waves
INWAVE

## Slide 49
INWAVE
FUTURE PLANS
INWAVE is not capable of including wave spectral variations along its boundaries and future efforts will be directed to include these capabilities.
We are still testing and verifying Inwave performance with model cases.

## Slide 50: INWAVE: THE INFRAGRAVITY WAVE DRIVER OF COAWST
COAWST WORKSHOP
Raleigh, 25th -28th February, 2019
Maitane Olabarrieta
John C. Warner
Christie Hegermiller