## Slide 1: Coupled model applications Tutorial
Projects/Sandy- Hurricane Sandy example

## Slide 2: - How does the coupled modeling system work (MCT) - SCRIP interpolation - Setting up a coupled application

## Slide 3: Why do we couple models?
Atmosphere
Wave
Ocean
Coastal
geomorphology
Usually treated independently but actually occur together

## Slide 4: Model setup
OCEAN
ATMOSPHERE
WAVE
us, vs, h, bath, Z0
Hwave, Lmwave, Lpwave, Dwave,
Dwavep, Tpsurf, Tmbott, Qb,
Dissbot, Disssurf, Disswcap,
Ubot
MCT
Uwind, Vwind, Patm, RH, Tair,
cloud, rain, evap, SWrad, Lwrad
LH, HFX, Ustress, Vstress
SST
MCT
Uwind, Vwind
Hwave, Lpwave, Tpsurf,
MCT
WRF wind speed
Longitude
Latitude
ROMS SST
SWAN Hsig
SEDIMENT
Ice
Biology
Vegetation

## Slide 5: OCN interactions
ATM
WAVE
Hwave, Lmwave, Lpwave, Dwave,
Tpsurf, Tmbott, Qb,
Dissbot, Disssurf, Disswcap,
Ubot
Uwind, Vwind, Patm, RH, Tair,
cloud, rain, evap, SWrad, Lwrad
LH, HFX, Ustress, Vstress
OCN
Integration and Application Network (ian.umces.edu/symbols),
University of Maryland Center for Environmental Science.
Uwind-ucur, Vwind-vcur,
Swrad, Lwrad,
RH, Tair,
cloud
Ustress, Vstress,
Swrad, Lwrad
LH, HFX
Patm
Use consistent stress roms+wrf
#define ATM2OCN_FLUXES
Use wrf vars in COARE
#define
BULK_FLUXES
rain, evap
Salt flux
Atm press
or
Hwave, Lmwave, Dwave,
Tpsurf, Qb,
Dissbot, Disssurf,
Disswcap,
Water column
Stokes + VF
Hwave, Lpwave, Dwave, Tpsurf,
Hwave, Lmwave, Dwave,
Tmbott, Ubot
Surface
Bottom
s= f ( Zos )
Zoa
t
b = f ( Zob )
t

## Slide 6: ATM interactions
OCN
ATM
WAV
SST
Hwave, Lpwave, Tpsurf,
Surface fluxes
Momentum
Heat
Moisture
= f ( Hwave, Lpwave, Tpsurf )
SST
OCN
WAV

## Slide 7
OCEAN SURFACE ROUGHNESS CLOSURE MODELS
TAYLOR & YELLAND 2001: TY2001
DRENNAN 2003: DGQH
OOST 2002: OOST
- Wave steepness based parameterization.
- Based on three datasets representing sea-state conditions ranging from strongly forced to shoaling.
- Wave age dependent formula but it also considers the effect of the wave steepness.
Wave age based formula to characterize the ocean roughness.
They combined data from many field experiments representing a variety of condition and grouped the data as a function of the wind friction velocity.
CHARNOCK 1955

## Slide 8: WAV interactions
1) Generation – wind speed forcing
is modified by ocean currents:
S(w) = f( Uwind – us ; Vwind – vs )
us, vs, h, bath, Z0
Uwind, Vwind
WAV
OCN
ATM
2) Propagation
– wave celerity in geographic space is modified by ocean currents
cx = cgx + us ; cy = cgy + vs
– change of wave direction (refraction) due to h, bathy, and currents:

## Slide 9
Model Coupling Toolkit
Mathematics and Computer Science Division Argonne National Laboratory
http://www-unix.mcs.anl.gov/mct/
MCT is an open-source package that provides MPI based communications between all nodes of a distributed memory modeling component system. Download and compile as libraries that are linked to.
Warner, J.C., Perlin, N., and Skyllingstad, E. (2008). Using the Model Coupling Toolkit to couple earth system models. Environmental Modeling and Software
Coupled Modeling System
Model A running on M nodes.
Model B running on N nodes.
Model C ………
(it also works here)
MCT provides
communications
between all models.
………

## Slide 10: Libraries
MCT - v2.60 or higher (distributed)
1) cd to the MCT dir
2) ./configure
This makes Makefile.conf. you can edit this file.
3) make
4) make install
5) set environment vars
setenv MCT_INCDIR COAWST/Lib/MCT/include
setenv MCT_LIBDIR COAWST/Lib/MCT/lib
(or where ever you installed them, see last slide)

## Slide 11: Compilers dir (side note)
?= means that it checks your environment first

## Slide 12: Model organization
master.F
mpi_init
init
run
finalize
init
run
finalize
{
{
SWAN
ROMS
init_file (# procs/model)

## Slide 13: init, run, and finalize
ROMS
SWAN
init
(grid decomp)
run
(sync. point)
finalize
init_param
init_parallel
init_scaclars
init_coupling
roms_init
roms_run
main3d
.....
waves_coupling
...
mpi_finalize
close_io
roms_finalize
MPI_INIT
SWINITMPI
SWMAIN
SWEXITMPI
SWINIT
SWREAD (grid)
init_coupling
swanmain
.....
ocean_coupling
...
mpi_finalize
close_io

## Slide 14: Grid decomposition (during initialization)
ROMS
SWAN
Each tile is on a
separate processor.
Each tile registers
with MCT.

## Slide 15: Determine what information to exchange
ROMS- init_coupling
SWAN- init_coupling
1
1
2
2
3
3
processed by each ROMS tile
processed by each SWAN tile

## Slide 16: Synchronization (run phase)
ROMS- ocean_coupling
SWAN- waves_coupling
MCT
MCT
processed by each ROMS tile
processed by each SWAN tile

## Slide 17: End phase
“master.F”
MPI barrier prevents program complete exit until all models arrive at this point.
Sometimes one model may die and other model is waiting.

## Slide 18: SCRIP grid interpolation
Needed when you run more than 1 model and the models are on different grids.
We started with SCRIP from LANL.
We adapted the code to read model grids, and write out one NetCDF file with all the interpolation weights.
We use the ‘group’ capability in NetCDF4.
http://oceans11.lanl.gov/trac/SCRIP

## Slide 19: 3) SCRIP - grid interpolation
Atmosphere model provides heat flux to cover entire ocean grid. SCRIP interpolations weights needed to remap data fields.
Ocean model provides higher resolution and coupled response of SST to atmosphere. But the ocean grid(s) are limited in spatial coverage so atmosphere model must combine data from different sources.
Flux conservative
remapping scheme
Ocean grid
Atm Grid
HFLX
10 GFS data
SST
Two main issues:
Interpolate data between different grids.
Combine data from different sources.

## Slide 20: Land masking effects – example of grid interpolation
Bottom stress (UST)
LANDMASK
This is a coarse example to demonstrate the effects of land/sea masking on atmospheric processes.
Large bottom stress over land will cause problems on an ocean grid with different masking.

## Slide 21: Grid interpolation
ATM land mask areas do not effect ocean.
WRF UST^2 over land + ocean
WRF UST^2 over ocean only
ROMS su/vstr over ocean only

## Slide 22: Combining multiple sources
Background GFS SST mask
ocn 1 to atm 1 mask
ocn 2 to atm 1 mask
Background GFS SST
ocn 1 SST
ocn 2 SST
Sum of all 3 masks = 1

## Slide 23: Combining multiple sources
Background GFS SST mask
ocn 1 to atm 1 mask
ocn 2 to atm 1 mask
Background GFS SST
ocn 1 SST
ocn 2 SST
Sum of all 3 masks = 1
SST Total

## Slide 24: SCRIP_COAWST
– based on SCRIP v 1.6 and modified to read scrip_coawst.in

## Slide 25: SCRIP_COAWST
1) cd to COAWST/Lib/SCRIP_COAWST
2) edit makefile
3) make
Set your compiler here
This will build the program “scrip_coawst”

## Slide 26: SCRIP_COAWST – input file
Output file name
Number of grids
for each model
ROMS grid names
SWAN grid names

## Slide 27: SCRIP_COAWST – input file
WRF grid names
SWAN grid names
Enter ‘moving’ for a moving nest.
Only the last WRF grid can be moving.

## Slide 28: SCRIP file(s)
Run the scrip coawst program using
./scrip_coawst scrip_coawst.in
We use NetCDF 4 functionality to create only 1 netcdf file using the ‘group’ functionality.
To read the data in matlab you can use (for example)
dst_grid2=ncread('scrip_sandy_static.nc','/ocn2_to_atm1_weights.nc/dst_grid_imask');
The old way: created a weight file between each grid.
So if you have 1 WRF grid, and 2 ROMS grids, it will produce
atm1_to_ocn1_weights.nc
atm1_to_ocn2_weights.nc
ocn1_to_atm1_weights.nc
ocn2_to_atm1_weights.nc

## Slide 29: Setting up a coupled application: Projects/Sandy

## Slide 30: How to create coupled application
1) Create all input, BC, init, forcing, etc files for each model as if running separately. I recommend that you run each model separately first.
2) SCRIP (if different grids or grid refinement)
3) modify cppdefs in your header file.
4) ocean.in, namelist.in, and coupling.in
5) coawst.bash
6) run it as coawstM

## Slide 31: 1) Use each model separately
WRF
  27 vertical levels
  dt 36 s
  Physics
    Lin microphysics
    RRTM longwave, Dudhia shortwave
    Mellor-Yamada-Janjic (MYJ) PBL
    …..
ROMS
  16 vertical levels
  dt 240, 48
  Physics
    GLS turbulence closure
    COARE bulk fluxes
    BC's from HYCOM
    …..

## Slide 32: 2) SCRIP
Edit the SCRIP input file:
COAWST/Lib/SCRIP_COAWST/scrip_coawst_sandy.in

## Slide 33: 2) SCRIP
Edit the SCRIP input file:
COAWST/Lib/SCRIP_COAWST/scrip_coawst_sandy.in

## Slide 34: 2) SCRIP
Run this in COAWST/Lib/SCRIP_COAWST
./scrip_coawst scrip_coawst_sandy.in
This will create one file called
OUTPUT_NCFILE='scrip_sandy_static.nc'

## Slide 35: 3) sandy.h
ROMS + WRF
application

## Slide 36: 4) coupling.in (this is a ROMS+WRF app)
set # procs for each model
set coupling interval.
Can be different for each direction.
input file names. only 1 for WRF, 1 for ROMS, multiple for SWAN
Projects/Sandy/coupling_sandy.in

## Slide 37: 4) coupling.in (this is a ROMS+WRF app)
SCRIP weights OPTION 1 or 2
SCRIP weights files names are listed here for Option 2
(multiple files, this option to be phased out.)
SCRIP weights files name listed here for Option 1
(single file)
NetCDF file uses “groups” feature so we need netcdf 4.

## Slide 38: 4) ocean.in
set # procs NtileI NtileJ
Model dt needs to divide evenly into the
coupling interval.

## Slide 39: 5) namelist.input
set # procs for atm model
need dt of 180 to divide
evenly into coupling interval
of 1800 sec.

## Slide 40: 6) run it as coawstM
use total number of procs from coupling.in
only 1 executable

## Slide 41: Processor allocation
stdout reports processor allocation
and
Number of steps between synchronization.
This looks like from a different run,
but you get the idea

## Slide 42: Processor allocation
"Timing for …." = WRF
"1 179 52974 02:59:00 " = ROMS
Here is where the model coupling synchronization occurs.
so probably could re-allocate more nodes to WRF

## Slide 43: Data field exchange min/max values
WRF 1 to ROMS 1
WRF 2 to ROMS 1
WRF 1 to ROMS 2
WRF 2 to ROMS 2